## Slide 1: COMBINATIONAL CIRCUITS

## Slide 2
Overview
  Introduction to Combinational Circuits
  Adder
  Ripple Carry Adder
  Subtraction
  Adder/Subtractor

## Slide 4: Adder
Design an Adder for 1-bit numbers
1. Specification: 2 inputs (X,Y) 2 outputs (C,S)

## Slide 5: Adder
Design an Adder for 1-bit numbers
1. Specification: 2 inputs (X,Y) 2 outputs (C,S)
2. Formulation:
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 6: Adder
Design an Adder for 1-bit numbers?
1. Specification: 3. Optimization/Circuit 2 inputs (X,Y) 2 outputs (C,S)
2. Formulation:
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 7: Half Adder
This adder is called a Half Adder
Q: Why?
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 8: Full Adder
A combinational circuit that adds 3 input bits to generate a Sum bit and a Carry bit

## Slide 9: Full Adder
A combinational circuit that adds 3 input bits to generate a Sum bit and a Carry bit
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
X
YZ
0
1
00 01 11 10
0 1 0 1
1 0 1 0
X
YZ
0
1
00 01 11 10
0 0 1 0
0 1 1 1
Sum
Carry
S = X’Y’Z + X’YZ’ + XY’Z’ +XYZ
= X  Y  Z
C = XY + YZ + XZ

## Slide 10: Full Adder = 2 Half Adders
Manipulating the Equations:
S = X  Y  Z
C = XY + XZ + YZ

## Slide 11: Full Adder = 2 Half Adders
Manipulating the Equations:
S = ( X  Y )  Z
C = XY + XZ + YZ
= XY + XYZ + XY’Z + X’YZ + XYZ
= XY( 1 + Z) + Z(XY’ + X’Y)
= XY + Z(X  Y )
OR:
S = ( X  Y )  Z
C = X’YZ + XY’Z + XYZ’ + XYZ
= (X’Y + XY’)Z + XY(Z+Z’)
= (X  Y )Z + XY

## Slide 12: Full Adder = 2 Half Adders
Manipulating the Equations:
S = ( X  Y )  Z
C = XY + XZ + YZ = XY + Z(X  Y )
Src: Mano’s Book
Think of Z as a carry in

## Slide 13: Bigger Adders
How to build an adder for n-bit numbers?
  Example: 4-Bit Adder
    Inputs ?
    Outputs ?
    What is the size of the truth table?
    How many functions to optimize?

## Slide 14: Bigger Adders
How to build an adder for n-bit numbers?
  Example: 4-Bit Adder
    Inputs ? 9 inputs
    Outputs ? 5 outputs
    What is the size of the truth table? 512 rows!
    How many functions to optimize? 5 functions

## Slide 15: Ripple Carry Adder
To add n-bit numbers:
Use n Full-Adders in parallel
The carries propagates as in addition by hand
Use Z in the circuit as a Cin
1 0 0 0
0 1 0 1
0 1 1 0
1 0 1 1

## Slide 16: Binary Parallel Adder
To add n-bit numbers:
Use n Full-Adders in parallel
The carries propagates as in addition by hand
This adder is called ripple carry adder
Src: Mano’s Book

## Slide 17: Subtractor
Design a Subtractor for 1-bit numbers
1. Specification: inputs (A, B) outputs (Diff, Borrow)

## Slide 18: Subtractor
Design a Subtractor for 1-bit numbers
1. Specification: inputs (A, B) outputs (Diff, Borrow)
2. Formulation:

## Slide 19: Half Subtractor
Design an Subtractor for 1-bit numbers
1. Specification: 3. Optimization/Circuit inputs (A, B) outputs (Diff, Borrow)
2. Formulation:
Diff
Borrow

## Slide 20: Full Subtractor
A full subtractor is a combinational circuit that performs subtraction of two bits, one is minuend and other is subtrahend, taking into account borrow of the previous adjacent lower minuend bit. This circuit has three inputs and two outputs.

## Slide 21: Full Subtractor
A
BBin
0
1
00 01 11 10
0 1 1 1
0 0 1 0
Borrow = A’B + BBin + A’Bin
A
BBin
0
1
00 01 11 10
0 1 0 1
1 0 1 0
Diff
Diff = A’B’Bin + A’BBin’ + AB’Bin’ + ABBin
= A  B  Bin
Borrow

## Slide 22: Full Subtractor = 2 Half Subtractors
Manipulating the Equations:
Diff = ( A  B )  Bin
Borrow = A’B + BBin + ABin
=
=
= A’B + Bin(A  B )’
OR:
Diff = ( A  B )  Bin
Borrow = A’B’Bin + A’BBin + A’BBin‘ + ABBin
= (A’B’ + AB)Bin + A’B(Bin + Bin’)
= (A  B )’Bin + A’B

## Slide 23: Full Subtractor = 2 Half Subtractors
Manipulating the Equations:
S = A  B  Bin
C = A’B + BBin + A’Bin

## Slide 24: Subtraction (2’s Complement)
How to build a subtractor using 2’s complement?

## Slide 25: Subtraction (2’s Complement)
How to build a subtractor using 2’s complement?
1
S = A + ( -B)
Src: Mano’s Book

## Slide 26: Adder/Subtractor
How to build a circuit that performs both addition and subtraction?

## Slide 27: Adder/Subtractor
Src: Mano’s Book
Using full adders and XOR we can build an Adder/Subtractor!
0 : Add
1: subtract

## Slide 28: Binary Parallel Adder (Again)
To add n-bit numbers:
Use n Full-Adders in parallel
The carries propagates as in addition by hand
This adder is called ripple carry adder
Src: Mano’s Book

## Slide 29: Carry Look Ahead Adder
How to reduce propagation delay of ripple carry adders?
Carry look ahead adder: All carries are computed as a function of C0 (independent of n !)
It works on the following standard principles:
  A carry bit is generated when both input bits Ai and Bi are 1, or
  When one of input bits is 1, and a carry in bit exists
Cn Cn-1…….Ci……….C2C1C0
An-1…….Ai……….A2A1A0
Bn-1…….Bi……….B2B1B0
Sn Sn-1…….Si……….S2S1S0
Carry Out
Carry bits